## Slide 1: ECE 492 Capstone Design: Multi-Functional Wireless Guitar
Group 4: Aaron Arnason, Byron Maroney, Edrick de Guzman

## Slide 2: Project Overview
The project has 4 main aspects:
  Digital Signal Processing
  Interfacing with Bluetooth Modules
  Live-streaming over TCP/IP sockets
  Power Amplifier with Passive Filtration (coming soon…)
Motivation
  Wireless Guitar Adapters are pricey
  No commercial solution that incorporates the functionality listed above

## Slide 3: What we’ve done so far…
Aaron
  Performed testing with the Guitar Signals
  Designed the architecture of the Main DSP
Byron
  Interfaced the Audio Circuitry with the NIOS II Processor
  Integration testing with the DSP
  Researched I2S protocol
Edrick
  Implemented Distortion effect in VHDL
  Tested the Distortion component in MATLAB and ModelSim
  Testing Reverberation effect in MATLAB

## Slide 4: Functionality: Hardware
DE2

## Slide 5: Functionality: Software

## Slide 6: Functionality
DSP
  The DSP can perform 3 effects
    1: Distortion (Clipping)
    2: Delay (Time-shifting)
    3: Reverberation (Adding dampened echoes)

## Slide 7: Functionality
Frequency Analyzer
  Required to implement the guitar tuner
    We need to find the fundamental frequency to determine the notes being played
    Can be accomplished using a Fast-Fourier Transform
    Mapping the frequencies to the notes will be done in software
      Need to use fixed-point arithmetic
String | Frequency | Scientific pitch notation
1 (E) | 329.63 Hz | E4
2 (B) | 246.94 Hz | B3
3 (G) | 196.00 Hz | G3
4 (D) | 146.83 Hz | D3
5 (A) | 110.00 Hz | A2
6 (E) | 82.41 Hz | E2

## Slide 8: Functionality
Bluetooth Module
  Transmits audio using A2DP (for high-quality audio) and AVRCP to select what effects we’re using
    Repurpose AVCRP signals
    Communicates with the Audio Codec (on the DE2) via I2S protocol
    The Bluetooth module is managed by the DE2 via the UART
  One of the modules will need to be pre-programmed

## Slide 9: Functionality
Web Server
  Audio data will be sent to remote web server using sockets over HTTP protocol
    Remote server will have to buffer the input
  Remote Web Server Implementation
    Not a design constraint (many web technology stacks exist)
    Currently favoring MEAN (MongoDB, Express, AngularJS, Node) Stack
      Easy to design, but mediocre performance

## Slide 10: Challenges
Buffering
  The data sent from the Bluetooth module uses I2S protocol.
    I2S is a continuous protocol (uses a single data line)
    The DSP input requires de-serialized data coming from the Bluetooth module
    DSP requires data to be re-serialized when sent to the Audio Codec
  Web server needs to buffer the audio stream to prevent “glitches”
Latency
  It’s difficult to play guitar if there’s a lot of latency
  Solution: Limit software, increase hardware usage
Load Balancing the Web Server

## Slide 11: Components List
Bluetooth Module
Frequency Analyzer
UART
DSP
Audio Codec
De-Serializer/Serializer
NIOS II
Ethernet MAC

## Slide 12: Code Example: DSP

## Slide 13: Code Example
Distortion Component

## Slide 14: Test Plan
Make sure audio core works
Make sure Guitar outputs at Line level
Test individual DSP components
  Distortion
  Reverberation
Serializer/De-serializer
Test implementation of I2S Protocol by directly interfacing with the audio codec
Make sure Bluetooth Component works
  Test Master/Slave Bluetooth configuration (ignore DE2)
  Test guitar signal over Bluetooth
  Test guitar tuner(sufficient resolution required)
  Test guitar effects
Streaming
  Test streaming audio over sockets (ignore Nios II)
  Test streaming audio over sockets (with Nios II)

## Slide 15: Optional Features
Automatic Tuning
Automatic Guitar Tab Generator
More Effects:
  Chorus
  Acoustic Simulator
  Equalizer
Infinity Mirror (Visualizer) [1] - https://en.wikipedia.org/wiki/Infinity_mirror#/media/File:Ultraviolet_infinity_mirro.jpg

## Slide 16: Questions
http://vignette3.wikia.nocookie.net/spore/images/6/6c/Question-mark.png/revision/latest?cb=20110427230528